ENTER PROGRAMMING MODE (without DAP)

Key in your 4 digit master code and press *. (Double conformation beep, amber light stays on indicating you are now in programming mode).

NOTE: The factory set master code in this keypad is 0000. It is recommended, in all cases, that a personal master code be programmed into the keypad to invalidate the factory set master code before use.

ENTER PROGRAMMING MODE USING DIRECT ACCESS PROGRAMMING (DAP)

If the personal master code is forgotten or lost the DAP jumper can be used to override the forgotten or lost code and permit the user direct entry into programming mode.

- Disconnect the power supply

- Move the DAP jumper from OFF to ON position

- Reconnect the power supply (continuous beeping, amber light flashes)

- Move the DAP jumper back to OFF position (Beeping stops, amber light stays on)

- The keypad is now in programming mode. As the old master code was forgotten we recommend that the first thing you do is enter a new 4 digit master code into location 0

SETTING NEW MASTER CODE

- Enter programming mode (Amber light stays on)

- Press 0 (The location of your master code)

- Key in your new 4 digit master code _ _ _ _

- Press # (Double conformation beep. Your new master code is now entered)

USER MODES

This keypad can be set for either single user or multi user.

TO SET KEYPAD TO SINGLE USER MODE:

- Enter programming mode (Amber light stays on)

- Key in 8900 and press # (Double conformation beep. Keypad is now set to single user)

TO SET KEYPAD TO MULTI USER MODE:

- Enter programming mode (Amber light stays on)

- Key in 8901 and press # (Double conformation beep. Keypad is now set to multi user)

IMPORTANT NOTE: When a user mode is set all of the data stored in the system apart from the master code will be cleared.

PROGRAMMING USER CODE (SINGLE USER)

In single user mode you can only use one 4 digit code for each output.

OUTPUT 1

- Enter programming mode (Amber light stays on)

- Press 1 (Selects output 1)

- Key in your 4 digit user code _ _ _ _

- Press # (Double conformation beep. Your user code for output 1 is now programmed)

OUTPUT 2

- Enter programming mode (Amber light stays on)

- Press 2 (Selects output 2)

- Key in your 4 digit user code _ _ _ _

- Press # (Double conformation beep. Your user code for output 2 is now programmed)

PROGRAMMING USER CODE (MULTI USER)

In multi user mode you can use up to 100 user codes for output 1 and up to 10 user codes for output 2.

OUTPUT 1

- Enter programming mode (Amber light stays on)

- Press 1 (Selects output 1)

- Select a user code location from 00 to 99

- Key in your 4 digit user code

- Press # (Double conformation beep. Your user code for output 1 is now programmed)

- Return to step 2 until all required user codes are entered

OUTPUT 2

- Enter programming mode (Amber light stays on)

- Press 2 (Selects output 2)

- Select a user code location from 0 to 9

- Key in your 4 digit user code

- Press # (Double conformation beep. Your user code for output 2 is now programmed)

- Return to step 2 until all required user codes are entered

PLEASE NOTE: when the user enters their code they must validate their entry by pressing the # key.

SETTING THE LOCK TIME

Both outputs 1 and 2 can be set to trigger for 1 to 999 seconds.

OUTPUT 1

- Enter programming mode (Amber light stays on)

- Press 4 0 (Selects duration code for output 1)

- Key in required latching time in seconds from 1 to 999

- Press # (Double conformation beep. Your user code for output 2 is now programmed)

OUTPUT 2

- Enter programming mode (Amber light stays on)

- Press 50 (Selects duration mode for output 2)

- Key in required latching time in seconds from 1 to 999

- Press # (Double conformation beep. Your user code for output 2 is now programmed)

EXIT PROGRAMMING MODE

To exit programming mode press * (Double conformation beep, amber light goes off)

NOTE: All programming can be done without having to exit and re enter programming mode